Current Electricity

CURRENT

- Current electricity is a flow of charged particles, usually through a circuit.

- In all conductors, the flow is of electrons and therefore of negative charge.

  - The electrons flow from a negative terminal to a positive terminal in a battery. They are attracted to the positive terminal and repelled from the negative terminal.

  - It was once thought that current flowed from positive to negative.

  - This was put forward by Benjamin Franklin (1706 – 1790) and it became so widely accepted that it is still accepted today and called conventional current, even though it was found to be wrong in 1898 when Sir Joseph J Thomson discovered the electron.

  - Consequently:

Though the electrons flow from negative to positive, conventional current flows from positive to negative (although conventional current doesn't really exist).

- Current is represented by the symbol, I, and is measured in amperes (amps or A) with an ammeter.

  - An ammeter measures the rate at which electrons are flowing through a circuit at a given point.

  - In a circuit, an ammeter is shown as follows:

  - One amp is equal to the flow of one Coulomb of charge per second. This translates to the following formula:

or,

  - Or in unit terms:

or,    		 1 A = 1 C/s

  - It turns out that:

  - where e represents the elementary charge (the charge on an electron)

e = 1.6 x 10-19 Coulombs

N = number of electrons

ELECTRIC POTENTIAL (VOLTAGE)

- In order for current to flow from point A to point B, a certain amount of work must be done on the charged particles.

- Alessandro Volta (1745 – 1827) was the first to demonstrate this with his invention of the battery in 1800.

- Electric potential is represented by the symbol, V, and is measured in volts (V) with an voltmeter.

  - A voltmeter measures the amount of electrical potential energy required to move a Coulomb of charge from one point to another in a circuit.

  - In a circuit, a voltmeter is shown as follows:

- The work required to move a Coulomb of charge from A to B is called the electric potential.

or,

- Or in unit terms:

or,    		 1 V = 1 J/C

ELECTRIC POTENTIAL ENERGY

- Recall:		Work is a transfer of energy!

- By rearranging the equation of electric potential, we now have the following:

or,

since

# Text boxes

A

V