Energy Efficiency

- A family uses several planks to slide a 350 kg piano onto the back of a pickup truck.  The box in the back of the pickup is 80.0 cm above the ground and the planks are 3.00 m long.  If an average force of 1500 N is required to slide the piano up the planks, find:

(a) the work done in loading the piano.

(b) the efficiency of the planks as a simple machine to load the piano.

- Several friends use a simple rope and pulley to raise a tree house from the ground into a tree.  The mass of the tree house is 150 kg.  By pulling together, the friends manage to exert an average force of 1.60 x 103 N as they raise the tree house a distance of 3.20 m above the ground.

  - Find the work done in raising the tree house.

  - How much “useful” work is done?

  - What is the efficiency of the rope and pulley in raising the tree house?

- A hydraulic lift at Vinnie’s Autobody & Collision shop is 47% efficient is in lifting a 1700 kg vehicle above the ground for an oil change.  If it takes the lift 12 seconds to lift the vehicle up to a height of 2.2 m, determine the power generated by the hydraulic lift.