Generating Electricity

Distribution of Electrical Power

Recall:

Sample Problem:

The following transformer has a primary voltage of 20 V.

- What is the secondary voltage?

- What is the secondary output current if the power dissipated in the transformer is 100 W?

Transmitting electrical energy over great distances from remote generating sites results in a loss of power.  This loss of power is primarily due to the overall resistance of the pathway.  This loss can be determined by the following equation:

P = I2R

Sample Problem:

Compare the power lost in transmission for a 1000 W line at 100 V to the same power on a line at 1000 V.  In both cases, the resistance of the line is 1 Ω.